## Slide 1: Gas Network modelling for a multi-gas system
Version July 12th, 2023

## Slide 2
Gas Network Model
Overview on Fluid-Dynamic Solver

## Slide 3: Gas Network Model
1D gas flow –
Transient –
Isothermal –
Multi-component –
Parameters
Inputs
– Gas Profiles
– P, Composition at injection node
– Network Topology
– Pipelines Features
Physical Model
Outputs
P, Composition – at each node
Gas Flow – for each branch
At each timestep
Coninutiy equation
Flow equation
Equation of State
determined through GERG-08
wide range equation of state
Closure equation:
Coupled equations to be linearized and solved iteratively
Overview:
Equations:
Notes: For these reasons, the model is based on one dimensional and transient flow equations, namely the conservation of mass and of momentum. The gas flow is assumed to be iso-thermal, which is a rather common and accepted simplification for gas network modeling througout the literature, thus the equation of concentration of energy is not necessary. In the end the multi-component feature is crucial for the purpose of multi-gas framework modeling.
The physical model needs to be provided with parameter of the gas network and operational data: concerning the parameter: the topology (the network structure, the connection between pipes) and the technical features of the pipes are needed; as of the operational data, the inputs, gas profiles at outlet nodes and pressure and composition values at the injection nodes are needed.

## Slide 4: Gas Network Model
Coninutiy equation
Flow equation
LINEARIZED EQUATION
Coupled fluid-dynamic problem
initial [t=0]
steady state solution
;
Equation of State
updates the fluid properties
Repeated for
each Timestep
Network Topology:
1
3
7
6
2
4
5
1
3
4
5
2
Incidence Matrix
representation of the network
+1 inlet node
-1 outled node
Reading column-by-column
branches
nodes
SIMPLE algorithm
adaptation
no
Solving Strategy:
Networkwide:

## Slide 5
Input data structure

## Slide 6: Input Data Structure – EDGE TABLE
branch | IN | OUT | L (km) | D (m) | epsi[mm] | COMP | REG | VAL | RES | n°Grid points
1 | 1 | 2 | 530.0 | 0.7937 | 0.014 |  |  |  |  | 53
2 | 2 | 3 | 1.0 | 0.7937 | 0.014 | 1 |  |  |  | 1
3 | 3 | 4 | 540.0 | 0.7937 | 0.014 |  |  |  |  | 54
nodes
Non pipeline elements
Either 0 or 1 to indicate that a specific branch is a Non-pipeline element thus the equations applied are different
Used to create a mesh within each pipe (used both for the fluiddynamic problem and more importantly, for the quality tracking)
Topological info:
Branch (edges) list and indication of inlet and oulet node
Non pipeline elements
Some additional column may be added as additional information about each pipe:
For example, to take into account the gravitational effect, if the altitude at each node is not available, then the DeltaH or the inclination angle should be indicated for each pipe
Non-pipeline (NP) elements have not been «structurally» embedded. The structure of the models allows for their integration but a more robust and general organization of the code and the integration of the NP elements should be done

## Slide 7: Input Data Structure – NODE TABLE
Node name | Node | Height [m] | Gas Flow [kW] | Pressure [bar-g] | CH4 | N2 | CO2 | C2H6 | C3H8 | H2 | … | H2S
Wafa | 1 | 0 | -5,203,292 | 100 | 85.306 | 3.882 | 1.268 | 6.486 | 2.058 | 0 | … | 0
Mellitah | 2 | 100 | 0 | 65 |  |  |  |  |  |  | … | 
Mellitah_out | 3 | 200 | 0 | 120 |  |  |  |  |  |  | … | 
Gela | 4 | 150 | 5,203,292 | 70 | 85.306 | 3.882 | 1.268 | 6.486 | 2.058 | 0.000 | … | 0.000
Some additional column may be added
For example, for graphical representation purposes, colums for x-y coordinates should be integrated
Vector of the molar composition of natural gas
Some additional column may be added here as well depending on the number of components of the natural gas we want to consider:
For quality tracking goals I would say that the minimum is 2
This should go together with the choice of the equation of state.
Usually the initial pressure is a given value as a boundary condition
Usually the outlet gas flow (here given in terms of thermal energy release) is a given value as a boundary condition
Sign convention:
+ if it is exiting form the network;
− If it is entering in the network
Others units my be accepted such as kg/s or Sm3/h

## Slide 8
Matlab Functions Management

## Slide 9
Matlab Functions Management
A_GRID CREATOR
Input PIPE
Input NODES
A_MODEL
It creates a .mat set of data about the infrastructure to avoid to always reading the data structures on Excel when working on the same infrastructure.
Given a topology, It is structured so that it is possible to set a number of points for each pipeline so to create a more refined topology of the network.
It is useful not only to obtain much precise fluid-dynamic results but also for the preparation of the batch method for quality tracking
DATA_INPUT_Trial2023_3.mat
Input Profiles
This is the model for the fluid-dynamic and quality tracking simulation of the network.
It reads from an excel file the time profiles of the set quantities at the boundary condition (pressure, mass flow, composition)
MOL2MASS_CONV
MolarMassGERG
MASS_HV
MASS2MOL_CONV
…
These are all functions that are called from the main script already in the preparation phase to calculate some useful quantities such as the molar mass, the mass based heating value and to convert molar concetration to mass and vice versa

## Slide 10
Matlab Functions Management
A_MODEL
Steady State
This function is called to calculate the initial condition of all the network simulation that is assumed to be in steady state.
This function uses the same solving algorithm for the fluid dynamic but the time dependent feature is set to 0
ReducingParametersGERG;
PseudoCriticalPointGERG;
PropertiesGERG
EQUATION OF STATE
(GERG-2008)
For any pressure of the gas in the network (the temperature is assumed to be always constant), all the other properties of the gas needs to be calculated.
There are many possible Equation of State that ones can call
GERG-2008 is the most advanced one but also the most computationally heavy.
The set of functions and subfunction were translated from a VBA tool available online by Marco Cavana, generating a quite complex system of functions and subfunctions, probably not the most efficient one.
One could think of structure the program to give a couple of choices to the final user on what is the desired Eq. Of State that is to be used
Other minor functions
Notes: To try and answer these questions, a gas network model was developed in order to simulate the transient behoviour of the gas network both in fluid-dynamic terms and from the point of view of the quality perturbation

## Slide 11
Matlab Functions Management
A_MODEL
Steady State
This function is called to calculate the initial condition of all the network simulation that is assumed to be in steady state.
This function uses the same solving algorithm for the fluid dynamic but the time dependent feature is set to 0
ReducingParametersGERG;
PseudoCriticalPointGERG;
PropertiesGERG
EQUATION OF STATE
(GERG-2008)
Other minor functions
OTHERS POSSIBLE ALGORITHM CAN BE IMPLEMENTED
In previous versions, the author used a different algorithm for the calculation of the steady state condition:
The SIMPLE algorithm adapted for the compressible fluid networks.
In general the SIMPLE algorithm is said to be very robust
We can think of implement it in the open access tool.

## Slide 12
Matlab Functions Management
A_MODEL
Steady State
This function is called to calculate the initial condition of all the network simulation that is assumed to be in steady state.
This function uses the same solving algorithm for the fluid dynamic but the time dependent feature is set to 0
ReducingParametersGERG;
PseudoCriticalPointGERG;
PropertiesGERG
EQUATION OF STATE
(GERG-2008)
Other minor functions
save('Trial2023_3_P0','p_0');
save('Trial2023_3_G0','G_0');
The calculation of the steady state gives
G0 = the mass flow rates at any pipeline (or pipeline section) of the network in the hypothesis that at t=1 the fluid-dynamic of the network is at steady state.
P_0 = the nodal pressure at any node of the network
These quantities are generally saved to save time when doing trials on the same network and starting from the same conditions

## Slide 13
Matlab Functions Management
A_MODEL
ReducingParametersGERG;
PseudoCriticalPointGERG;
PropertiesGERG
EQUATION OF STATE
(GERG-2008)
Other minor functions
Getting into the fluid-dynamic simulation phase:
Frictionfactoraverage
Viscosity Calculator
The calculation of the friction factor for each pipeline section is done calling an outside function. As it is funciton of the Reynolds Number that, in turn, in funciton of the viscosity calculator, also the viscosity is calculated through an external function as it is variable with the composition and the temperature.
The correlations for the friction factor are many and as for the equation of state, we could decide if setting up different choice.
In any case this friction factor calculator is quite light computationally speaking

## Slide 14
Matlab Functions Management
A_MODEL
ReducingParametersGERG;
PseudoCriticalPointGERG;
PropertiesGERG
EQUATION OF STATE
(GERG-2008)
Other minor functions
Getting into the fluid-dynamic simulation phase:
Frictionfactoraverage
Viscosity Calculator
This is the part of the program that is nested in 2/3 cycle:
TIME: if the simulation is time-dependent, any consequent instant of time is solved starting from the solution of the previous timestep (it is the «ii» cycle with reference to the matlab script)
COMPOSITION it is cycled util the gas quality problem reaches a convergence: this to take into account the impact of the change of the gas composition on the fluid dynamic TO BE CHECKED + TO BE CHECKED IF THIS CYCLE IS MEANINGFUL AT THE MOMENT IS NOT INCLUDED.
Convergence of the linearization of the fluid-dynamic problem this is the «k» cycle (with reference to the matlab script) where all what has been discussed and will be described is cycled.

## Slide 15
Deep dive into the fluid-dynamic equations

## Slide 16: Transient Gas Network Model
Coninutiy equation
Flow equation
A closer look:
creeping motion
cv
Control Volume integration
horizontal pipelines
Finite Difference over a pipeline
with:
Fluid-dynamic
Resistance
Inertia
Resistance
Friction factor  Colebrook-White correlation
Compressibility Factor  GERG-2008 wide range equation of state
Averaged over the pipeline length
time discretization
LINEARIZATION NEEDED!
time discretization

## Slide 17: Detail of momentum eq. with gravitational term
Flow equation
creeping motion
integration of the spatial derivative:
linear and non-homogeneous differential equation
average pressure
Effective length
average speed of
Sound
Gas composition
Averaged quantities which makes possible the analytical solution

## Slide 18: Detail of momentum eq. with gravitational term
with:
Fluid-dynamic
Resistance
Inertia
Resistance
Averaged over the pipeline length
LINEARIZATION NEEDED!
Ordinary differential equation in which time derivative (inertia term) can be trated by means of implicit finite different scheme (over each pipe)
For a generic pipe j, assuming the
linearization point as ,
the application of the linearization formula:
leads to the following expression:
LINEARIZATION FORMULA

## Slide 19: Detail of momentum eq. with gravitational term
Dividing by:

## Slide 20: Matrix construction (momentum eq)
Pipeline linearized equation
Modified incidence matrix
to take into account the gravitational terms (referred to the squared pressures)
Aminus_s=Aminus.*repmat(exp(s),1,dimn)'
ADP=(-Aminus_s+Aplus)'
Aminus_s1=Aminus.*repmat(exp(s/2),1,dimn)'
ADP1=(-Aminus_s1+Aplus)'
Pipeline linearized equation
Modified incidence matrix
to take into account the gravitational terms (referred to the pressures)
unknowns
Element by element division
 element by element product

## Slide 21: Matrix construction (momentum eq)
Pipeline linearized equation
unknowns
Element by element division
ADP
-R_k
n
b
b
momentum equation
p
G
n
b
1
=
TN_M_k
b
1
b x n
n x 1
b x b
b x 1
b x b
b x 1
b x b
b x 1

## Slide 22: Matrix construction (continuity eq)
cv
n x 1
b x 1
unknowns
n x 1
n x 1
In this paper here: https://doi.org/10.1016/j.jngse.2015.11.036
They use this methodology for the boundary conditions:
When I tried to implement this I was obtaining oscillating behaviours.

## Slide 23: Matrix construction (continuity eq)
PHI
Ap
II
n
n
b
n
Continuity equation
p
G
n
b
1
=
TN_p
1
cv
G_ext/
p_fixed
n
n
n x n
n x 1
n x b
b x 1
unknowns
n x n
n x 1
n x n
n x 1

## Slide 24: Matrix construction
PHI
Ap
II
ADP
-R_k
0
0
n
n
b
n
b
n
Diagonal matrix
Continuity equation
momentum equation
boundary conditions
p
G
G_ext
n
b
n
1
=
TN_p
TN_M_k
TN_L
n
b
n
1
TN_P=PHI*p_n;
%TN_P=PHI*p_n-II./2*L_0(:,ii-1);
TN_M_k=(-Rf.*abs(G_k(:,k)).*G_k(:,k) -Ri.*G_n);
TN_L=G_ext_t(:,ii); TN_L(1)=p_in_t(ii)
From matlab code
1 or 0 on the diagonals to fix
PRESSURE OR MASS FLOW
at the designated nodes
Assigned pressure or mass flow (either inlet or outlet) accrodingly

## Slide 25: Gas Network Model – overview of the fluid-dynamic solver
Coninutiy equation
Flow equation
LINEARIZED EQUATION
Coupled fluid-dynamic problem
initial [t=0]
steady state solution
;
Equation of State
updates the fluid properties
Repeated for
each Timestep
Network Topology:
1
3
7
6
2
4
5
1
3
4
5
2
Incidence Matrix
representation of the network
+1 inlet node
-1 outled node
Reading column-by-column
branches
nodes
no
Solving Strategy:
Networkwide:

## Slide 26
Quality Tracking section
For the moment I am stopping here: in the following slide I gave to you just the overview of the method used. I need to revise more carefully the different version I created.
In any case I always found it hard to model this “batch method” and I would appreciate if we could work together, even starting from almost scratch, in order to create a tool that is much more efficient than the one I used to have.
After all, I think that the application of the batch method is, at least for the case of each pipeline, a problem that can be formalized as a “queue problem”. It needs to be coupled with conservation of mass at the intersections.

## Slide 27: Validation
Convergence of fluid-dynamic problem
Advective transport equation
with:
– : gas velocity;
– : gas composition vector;
Lagrangian coordinates-based BATCH TRACKING METHOD
 Transport of the concentration vector along the pipelines
 Mixing at network nodes
Coninutiy equation
for each chemical species
Coninutiy equation
Back to coupled fluid-dynamic problem
Advective transport equation
for each branch connecting two mixing nodes
no
Repeated for
each Timestep
Quality Tracking section:
Solving strategy:

## Slide 28
To be continued…